## Slide 1
SPS 330.07(9)
Assure that training and education involving live fire fighting exercises meet the standards specified in NFPA 1403.
Notes: Hello everyone. My name is Steve Komar and I am District 4’s Fire Prevention Coordinator and in this presentation, I will be discussing the most current standard on live fire training the 2018 edition of NFPA 1403
And as I review this standard with you please keep in mind that I will not be going through every component of this standard due to time. I will just be highlighting some of the important aspects of this live fire training standard. As you will see, the common theme to this standard is to provide a safe & healthy environment for all members of the fire department as well as the community. So, if you plan to hold a live fire training, it shall be in compliance with the most current edition of NFPA 1403 because Wisconsin Administrative Rule SPS 330 states to “assure that training and education involving live fire fighting exercises meet the standards specified in NFPA 1403”.

## Slide 2
This standard shall contain the minimum requirements for training all fire suppression personnel engaged in fire-fighting operations under live fire conditions.
The purpose of this standard shall be to provide a process for conducting live fire training evolutions to ensure that training objectives are achieved and that exposure to health and safety hazards for the fire fighters receiving the training is minimized.
Live fire training shall only be conducted using standard operating procedures (SOPs) developed by the authority having jurisdiction in compliance with this standard.
Notes: *1403 contains the minimum requirements for training all fire suppression personnel engaged in fire-fighting operations under live fire conditions.
*And the purpose of this standard is to provide a process for conducting live fire training evolutions to ensure that the training objectives are achieved and that exposure to health and safety hazards for the fire fighters receiving the training is minimized.
*Live fire training shall only be conducted using SOPs developed by the AHJ in compliance with this standard.

## Slide 3
General
Strict safety practices shall be applied to all structures selected for live fire training evolutions.
All required permits to conduct live fire training evolutions shall be obtained.
Notes: *Strict safety practices need to be applied to all structures selected for live fire training.
* And all required permits to conduct live fire training shall be obtained.

## Slide 4
Fire department training structure burns
  If the burning includes a building, submit a demolition notification to the DNR Asbestos Removal and Notification Program.
  Remove all material containing asbestos, so as to be in compliance with ch. NR 447, Wis. Adm. Code.
  Remove asphalt shingles and asphalt and plastic siding unless these materials are considered necessary to the fire department practice.
  Obtain any necessary burning permits. If the structure is in an incorporated city or village, check local ordinances and requirements.
  Dispose of ash from the burned structure, when cool, in a landfill approved by the DNR. The DNR may approve alternate ash disposal sites if groundwater and surface water quality will not be affected.
Notes: WI Dept of Natural Resources regulations allow fire departments to burn structures for staff or equipment training purposes. You will need to complete the following steps with regards to the DNR:
*You need to submit a demolition notification to the DNR Asbestos Removal and Notification Program. Removing all materials containing asbestos, to be in compliance with WI Admin Code.
*You need to remove asphalt shingles and asphalt and plastic siding unless these materials are considered necessary to the fire department practice.
*You will need to obtain any necessary burning permits. If its in an incorporated municipality, you will need to check local ordinances and requirements.
*And any ash from the burned structure needs to be dispose of in a landfill approved by the DNR.

## Slide 5
Required Minimum Training.
Prior to being permitted to participate in live fire training evolutions, the student shall have received training to meet the minimum job performance requirements for Fire Fighter I in NFPA 1001 related to the following subjects:
  (1)Safety
  (2)Fire behavior
  (3)Portable extinguishers
  (4)Personal protective equipment (PPE)
  (5)Ladders
  (6)Fire hose, appliances, and streams
  (7)Overhaul
  (8)Water supply
  (9)Ventilation
  (10)Forcible entry
  (11)Building construction
Student Prerequisites
Notes: *So Prior to being permitted to participate in live fire training evolutions, the student shall have received training to meet the minimum job performance requirements for Fire Fighter I related to these following 11 subjects: No need to say them
  (1)Safety
  (2)Fire behavior
  (3)Portable extinguishers
  (4)PPE
  (5)Ladders
  (6)Fire hose, appliances, and streams
  (7)Overhaul
  (8)Water supply
  (9)Ventilation
  (10)Forcible entry
  (11)Building construction

## Slide 6
Documentation of Prescribed Minimum Training.
  All participants in a live fire training evolution who have received the required minimum training from other than the AHJ shall not be permitted to participate in any live fire training evolution without first presenting written evidence of having successfully completed the prescribed minimum training to the levels specified in 4.3.1.
Notes: *All participants in a live fire training evolution who have received the required minimum training from other than the AHJ shall not be permitted to participate in any live fire training evolution without first presenting written evidence of having successfully completed the prescribed minimum training of the previous slide.

## Slide 7
Prerequisites for Live Fire Training Participants.
Fire Dynamics
Health and Safety
Fundamentals of Fire Behavior
Fire Development in a Compartment
Nozzle Techniques and Door Control
Notes: Prior to being permitted to participate in live fire training, all participants shall have received training to meet the requirements of the following:
Fire Dynamics.
  So, things like the conditions necessary for flashover to occur
  The components of fire and the three mechanisms of heat transfer.
All participants shall have received training of Health and Safety.
  So the components, capabilities and limitations of their protective clothing and equipment
All participants shall have received training of the Fundamentals of Fire Behavior.
  Things like basic chemical and physical processes involved in combustion
  The fire triangle and fire tetrahedron.
  The basic concepts of thermal dynamics
  ETC.
All participants shall have received training of Fire Development in a Compartment.
  So, the general development of a fire and extension beyond a single room or compartment, and building factors influencing fire development
And all participants shall have received training of Nozzle Techniques and Door Control.
  So, things like the Factors influencing the effectiveness of extinguishment by cooling
  The application of indirect attack and direct attack
  Effective door entry and control procedures

## Slide 8
Participant Health and Safety.
Nature of the work to be performed by the participant
Physical stress of the work on the participant
Temperature of the work and evolution environment
Exposure time in a high temperature environment, and
Other circumstances (e.g. weather, heat index)
Notes: It says in the standard that Instructors and participants need to be rehabbed in accordance with the provisions of NFPA 1584. Something to keep in mind throughout this standard is that there are many secondary references that are not adopted by the State of Wisconsin. This is an example of a secondary reference, so it is not adopted by the State of Wisconsin but is best practice.
When assessing the length and number of live fire training sessions or evolutions conducted in a training day, the following should be considered:
  *(1)Nature of the work to be performed by the participant,
  *(2)Physical stress of the work on the participant,
  *(3)Temperature of the work and evolution environment
  *(4)Exposure time in a high temperature environment, and
  *(5)And then other circumstances such as weather and heat index.
If asked
Subchapter IV — Adopted Standards
SPS 330.02 Incorporation of standards by reference. The following standards are incorporated by reference into this chapter:
(1) NFPA 1001-2013, Standard for Fire Fighter Professional Qualifications.
(2) NFPA 1002-2017, Standard for Fire Apparatus Driver/Operator Professional Qualifications.
(3) NFPA 1021-2014, Standard for Fire Officer Professional Qualifications, subject to the modifications specified in this chapter.
(4) NFPA 1403-2018, Standard on Live Fire Training Evolutions.
(5) NFPA 1901-2016, Standard for Automotive Fire Apparatus.
(6) NFPA 1911-2017, Standard for the Inspection, Maintenance, Testing, and Retirement of In-Service Emergency Vehicles, subject to the modifications specified in this chapter.
(7) NFPA 1971-2018, Standard on Protective Ensembles for Structural Fire Fighting and Proximity Fire Fighting.
(8) NFPA 1981-2013, Standard on Open-Circuit Self-Contained Breathing Apparatus for Emergency Services.
(9) NFPA 1982-2013, Standard on Personal Alert Safety Systems (PASS).
(10) NFPA 1983-2017, Standard on Life Safety Rope and Equipment for Emergency Services, subject to the modifications specified in this chapter.
(11) CGA Standard G-7.1, 2011, Commodity Specification for Air.

## Slide 9
Extreme Weather.
The training session shall be curtailed, postponed, or canceled, as necessary, to reduce the risk of injury or illness caused by extreme weather conditions.
Notes: *The training session shall be curtailed, postponed, or canceled, as necessary, to reduce the risk of injury or illness caused by extreme weather conditions.

## Slide 10
Safety Officer
A safety officer shall be appointed for all live fire training evolutions.
                (1)Prevention of unsafe acts
                (2)Elimination of unsafe conditions
Notes: *A safety officer shall be appointed for all live fire training.
All live fire training instructors and safety officers shall be trained on the requirements contained in 1403.
The safety officer shall have the authority, regardless of rank, to intervene and control any aspect of the operations when, in his or her judgment, a potential or actual danger, potential for accident, or unsafe condition exists.
The responsibilities of the safety officer shall include, but not be limited to:
  *(1)The Prevention of unsafe acts and,
  *(2)The Elimination of unsafe conditions
The safety officer needs to provide for the safety of all people on the scene, including students, instructors, as well as visitors and spectators.
The safety officer should not be assigned other duties that interfere with safety responsibilities.
The safety officer shall be knowledgeable in the operation and location of safety features available so things like emergency shutoff switches, gas shutoff valves, and evacuation alarms.

## Slide 11
Instructor-in-Charge and Instructors
Notes: This standard says that the instructor shall meet the minimum job performance requirements for Fire Instructor I and The instructor-in-charge shall meet the minimum job performance requirements for Fire Instructor II in NFPA 1041. So again, to be clear, this is a Secondary reference and is not adopted by the State of Wisconsin, but it is best practice.
It needs to be the responsibility of the instructor-in-charge to coordinate overall fireground activities to ensure correct levels of safety.
The instructor-in-charge needs to assign the following personnel:
(1)One instructor to each functional crew, each of which shall not exceed five students
(2)One instructor to each backup line and,
(3)One additional instructor for each additional functional assignment
The instructor-in-charge shall provide for rest and rehab of participants operating at the scene, including any necessary medical evaluation and treatment, food and fluid replenishment, and relief from climatic conditions.
There are many more requirements for Instructor in charge and instructors within this standard that I am not going to go over due to time so please do your homework.

## Slide 12
Water Supply
Notes: The instructor-in-charge and the safety officer need to determine the rate and duration of waterflow necessary for each individual live fire training evolution, including the water necessary for control and extinguishment of the training fire, the water supply necessary for backup line(s) to protect personnel, and any water needed to protect any exposed property's.
Each hose line and backup line shall be capable of delivering a minimum of 95 gpm.
A minimum reserve of additional water in the amount of 50 percent of the fire flow demand, needs to be available to handle exposure protection or any unforeseen situations.
And separate water sources needs to be utilized for the supply of attack lines and backup lines in order to preclude the loss of both water supply sources at the same time.

## Slide 13
Fire Control Team
Notes: A fire control team needs to consist of a minimum of two personnel.
1. One person who is not a student or the safety officer shall be designated as the “ignition officer” to ignite, maintain, and control the materials being burned.
2. And one member of the fire control team has to be in the area to observe the ignition officer ignite and maintain the fire, and to recognize, report, and respond to any adverse conditions.
The fire needs to be ignited by the ignition officer.
The decision to ignite the training fire needs to be made by the instructor-in-charge in coordination with the safety officer.
The fire control team needs to wear full protective clothing, including SCBA, when performing this function.
And a charged hose line needs to be available when the fire control team is igniting or tending to any fire.

## Slide 14
Personal Protective Clothing.
Secondary Reference (Best Practice)
Adopted
Notes: All students, instructors, safety personnel, and any other personnel involved shall all wear protective clothing and equipment according to manufacturer’s instructions whenever they’re involved in any evolution or fire suppression operation during the live fire training.
The standard says that the safety officer needs to ensure that all participants’ PPE has been inspected in accordance with NFPA 1851 and 1852 prior to entry into a live fire training evolution to verify that the protective clothing and SCBA are being worn correctly and are in serviceable condition. Again, these NFPA standards are Secondary references which are not adopted by the State but they are best practice.
Where station or work uniforms are worn by any participant, the station or work uniform shall have been manufactured to meet the requirements of NFPA 1975. This again is a Secondary reference which is not adopted by the Sate but is best practice.
Protective coats, trousers, hoods, footwear, helmets, and gloves shall have been manufactured to meet the requirements of NFPA 1971. 1971 is an adopted standard in the State of Wisconsin so it must be followed.
1403 says that the fire department shall provide and require all students, instructors, safety personnel, and any other personnel participating in any evolution or operation of fire suppression during the live fire training evolution to use SCBA when engaged in any operation where they could encounter atmospheres that are IDLH or potentially IDLH or where the atmosphere is unknown.
1403 says that SCBA shall have been manufactured to meet the requirements of NFPA 1981. Now this is an adopted standard in the State of Wisconsin so it must be followed.
And PASS devices shall have been manufactured to meet the requirements of NFPA 1982. This again is an adopted standard in the State of Wisconsin

## Slide 15
Communication
Notes: A method of fireground communications needs to be established to enable coordination among the incident commander, the interior and exterior sectors, the safety officer, and any external requests for assistance.
And a building evacuation plan needs to be established, including an evacuation signal to be demonstrated to all participants in an interior live fire training.

## Slide 16
Fuel Materials
Notes: The fuels that are utilized in live fire training shall only be wood products.
Pressure-treated wood is not allowed as well as rubber, plastic, polyurethane foam, tar paper, upholstered furniture, carpeting, and chemically treated or pesticide-treated straw or hay shall not be used as part of the fuel load.
Flammable or combustible liquids shall not be used in live fire training. Though combustible liquid with a flash point above 100°F shall be permitted to be used only in a live fire training structure or prop that has been specifically engineered to accommodate a defined quantity of the fuel.
Propane or butane lighters, safety flares, and other similar devices are permitted to be used to ignite training fires if the device is obviously removed immediately after ignition of the training fire.
Fuel materials needs to be used only in the amounts necessary to create the desired fire size.
The fuel load needs to be limited to avoid conditions that could cause an uncontrolled flashover or backdraft. And If a controlled flashover is designed to occur for training purposes, additional safety measures for providing a safe observation space for instructors and students needs to be documented and followed.
And the instructor-in-charge and the safety officer needs to document fuel loading, including all of the following:
  (1)Fuel material
  (2)Wall, floor coverings and ceiling materials
  (3)Type of construction of the structure, including type of roof and combustible void spaces
  (4)And the Dimensions of the room

## Slide 17
Parking/Staging
Notes: Areas for the parking, staging, and operating of fire apparatus that are used in the live fire trainings needs to be designated.
An area for parking fire apparatus and vehicles that are not a part of the evolution needs to be designated so as not to interfere with fireground operations.
If any of the apparatus is in service to respond to an emergency, they needs to be in an area that will facilitate a prompt response and ingress and egress routes needs to be designated, identified, and monitored during the training to ensure their availability in the event of an emergency.
Where required or necessary, parking areas for police vehicles or for the press needs to be designated.

## Slide 18
Emergency Medical Services
Notes: BLS emergency medical services with transport capabilities needs to be available on site to handle injuries.
A parking area for emergency medical services vehicle(s) needs to be designated and located where it will facilitate a prompt response in the event of a personal injury to participants in the evolution.
And written reports needs to be completed and submitted on all injuries and on all medical aid rendered.

## Slide 19
Visitors and Spectators
Notes: All visitors and spectators shall be restricted to an area outside the operations area perimeter established by the safety officer.
And control measures need to be established to keep pedestrian traffic in the vicinity of the training site clear of the operations area of the live burn.

## Slide 20
Preburn Plan/Briefing
Notes: A preburn plan needs to be prepared and needs to be utilized during a preburn briefing sessions.
All features of the training areas need to be indicated on the preburn plan.
Prior to conducting actual live fire training evolutions, a preburn briefing session needs to be conducted by the instructor-in-charge with the safety officer for all participants.
I am not going to go through all of the requirements of this section to save time so once again please do your homework.

## Slide 21
Victim(s)
Notes: If you plan to use victims in your training remember this statement in 1403:
No person or persons shall play the role of a victim inside any live fire training structure or acquired structure. I am going to say it again; No person or persons shall play the role of a victim inside any live fire training structure or acquired structure.
A rescue manikin can be used. Rescue manikins dressed in fire-fighting personal protective clothing and used as victims shall be uniquely colored or specially marked such as a Hi-Viz vest.

## Slide 22
Acquired Structures
Notes: Any acquired structure that is considered for a structural fire training exercise needs to be prepared for the live fire training evolution.
Buildings that cannot be made safe as required by this standard shall not be utilized for interior live fire training evolutions.
Preparation needs to include the application for and receipt of required permits and permissions.
Ownership of the acquired structure needs to be determined prior to its acceptance by the AHJ.
Evidence of clear title is required.
Written permission needs to be secured from the owner of the structure in order for the fire department to conduct live fire training evolutions.
A clear description of the anticipated condition of the acquired structure at the completion of the training and the method of returning the property to the owner needs to be put in writing and acknowledged by the owner of the structure.
Proof of insurance cancellation or a signed statement of nonexistence of insurance needs to be provided by the owner of the structure prior to acceptance by the AHJ.
A search of the acquired structure needs to be conducted to ensure that no unauthorized persons, animals, or objects are in the acquired structure immediately prior to ignition. Imagine if we burned a building down and kids were messing around and hiding in the attic.
Only one fire at a time shall be permitted within an acquired structure.
In preparation for live fire training, an inspection of the structure shall be made to determine that the floors, walls, stairs, and other structural components can withstand the weight of contents, participants, and accumulated water.
Closed containers and highly combustible materials needs to be removed from the structure.
Oil tanks and similar closed vessels that cannot be removed needs to be vented to prevent an explosion or overpressure rupture and any hazardous or combustible atmosphere within the tank or vessel needs to be rendered inert.
There are many other details like this in the standard such as chimney removal, vegetation removal, insect hive removal, disconnecting utilities, etc. but I am going to move on.

## Slide 23
Gas-Fired Live Fire Training Structures and Mobile Enclosed Live Fire Training Props
Non-Gas-Fired Live Fire Training Structures and Mobile Enclosed Live Fire Training Props
Exterior Live Fire Training Props
Notes: Please keep in mind that NFPA 1403 also covers the standards for :
Gas-Fired and Non-Gas-Fired Live Fire Training Structures and Mobile Enclosed Live Fire Training Props as well as
Exterior Live Fire Training Props

## Slide 24
Reports and Records
Notes: The reports and records here needs to be maintained on all live fire training in accordance with the requirements of 1403 which include:
(1)An accounting of the activities conducted
(2)A listing of instructors present and their assignments
(3)A listing of all other participants
(4)Documentation of unusual conditions encountered
(5)Any injuries incurred, and treatment rendered
(6)Any changes or deterioration of the structure
(7) And Documentation of the condition of the premises and adjacent area at the conclusion of the training exercise
Records pertaining to the structure shall be completed which we talked about earlier regarding owner permission and proof of insurance cancelation.
Upon completion of the training session, an acquired structure shall be formally turned over to the control of the property owner and shall include the completion of a standard form indicating the transfer of authority for the acquired structure.
And a post-training critique session, complete with documentation, needs to be conducted to evaluate student performance and to reinforce the training that was covered.

## Slide 25
Notes: So, to conclude here, please remember that this is a brief overview of NFPA 1403 and I highly encourage anyone that is planning a live fire training to read and follow this standard. This standard is for the safety & health of each and every participant as well as the community that you serve.