|  | STATE OF WISCONSIN Department of Safety and Professional Services Elevator Safety Program 141 NW Barstow Street, 4th Floor. Waukesha WI 53188 |  |
| --- | --- | --- |

# New (Acceptance) Commercial Stairway Chairlift Inspection Checklist

# This completed checklist (meeting A17.1, 8.10.1.1.5) and applicable test reports are to be included with the acceptance test records required by A17.1, 8.6.1.4.1(d) and are to be permanently available and located as required by SPS 318.1708(2)(b) 4.

| Date: | Regulated Object ID no: | Project Description: |
| --- | --- | --- |
| Inspector Name: | WI license no: | Exp. Date: | (also QEI certified) |
| Elev. Contractor Name: |  |  | [Stat. 101.984(2), SPS 305.993-999] |
| Elevator or Lift Mech. Name: | WI license no: | Exp. Date: | [Stat. 101.984(1), SPS 305.9905] |
| Permit application form, approved plans and conditional approval letter visible upon arrival Application form, plans and conditional approval letter checked for unique conditions |  | [Stat. 101.983(1)(b) and (2)(d), and SPS 318.1008(4)] |
| Rated load (lbs) | Rated speed up (actual, fpm) | Rated / Oper speed down (actual, fpm) |

| SUBJECT | STATUS | CODE | SUBJECT | STATUS | CODE |
| --- | --- | --- | --- | --- | --- |
|  | P | F | NA |  |  | P | F | NA |  |
| Available egress width agreeing with approved plans – measured with lift in unfolded, usable position |  |  |  | A18.1, 4.1.1, 362.1009, SPS 318.1804 |  |  |  |  |  |
| Guarding for remotely located driving machine |  |  |  | A18.1, 4.3.5 |  |  |  |  |  |
| Chair and seat, swivel seat where required |  |  |  | A18.1, 4.6 |  |  |  |  |  |
| Footrest obstruction device |  |  |  | A18.1, 4.6.3 | Documentation |
| Footrest clearance |  |  |  | A18.1, 4.6.4 | Green object ID no. tag applied by inspector |  |  |  |  |
| Rated load not less than 250 lbs |  |  |  | A18.1, 4.7.1 | Accident reporting tag applied by inspector |  |  |  |  |
| Rated speed not exceeding 40 fpm |  |  |  | A18.1, 4.7.1 | Operation and maintenance instructions |  |  |  | A18.1, 11 |
| Capacity and data plates |  |  |  | A18.1, 4.7.3, 4 | Maintenance control program |  |  |  | A18.1, 11.1 |
| Safety device type - 75 fpm max trip speed. (Can be tripped at normal speed for test) |  |  |  | A18.1, 4.8 |  |  |  |  |  |
| Safety device application mechanical only |  |  |  | A18.1, 4.8.3 |  |  |  |  |  |
| Safety device application – chair level |  |  |  | A18.1, 4.8.3.1 |  |  |  |  |  |
| Normal and final terminal stopping devices |  |  |  | A18.1, 4.9 |  |  |  |  |  |
| Code data plate (No Sharpie) |  |  |  | A18.1, 4.11 |  |  |  |  |  |